## Slide 1: Substream-Centric Maximum Matchings on FPGA
Maciej Besta, Marc Fischer, Tal Ben-Nun, Johannes de Fine Licht, Torsten Hoefler

## Slide 2: Large graphs…
Why do we care?
Social networks
Engineering networks
Useful model
Biological networks
Physics, chemistry
Communication networks
...even philosophy 
Machine learning

## Slide 3: Large graphs…
One particularly important problem
Matching: A set of edges such that no two edges share a common vertex
Maximum Weighted Matching (MWM): A matching such that the sum of the edge weights is maximized
10
10
10
5
5
5
10
10
10
5
5
5
Weight = 30
Weight = 15
2-approximation: here, we have a
2-approximation (30/15 = 2)
Approximate MWMs are crucial to many problems
Why do we care?
Scheduling
Transplant matching
Traveling Salesman Problem
Many, many others...
In all cases, approximations („reasonably” accurate) are useful
[Quantum] error correcting codes
“We live in a system of approximations” — Ralph Waldo Emerson

## Slide 4: Research Questions
Which programming paradigm to use for (approximate) MWM
(and other graph problems)?
How to design a high-performance MWM algorithm (as dictated by the used paradigm)?
What is the HW FPGA design that ensures high performance?
What is the ultimate performance, power consumption, and the related tradeoffs?

## Slide 5
What programming paradigm and why?
Key techniques, paradigms, challenges, features, …
Selected parts are in the FPGA paper, the rest is in…
~25 FPGA accelerators for specific algorithms
~15 FPGA graph processing frameworks
Part 1: Seeking “the best paradigm”, we conducted a detailed analysis of graph processing on FPGAs
http://spcl.inf.ethz.ch/Publications/.pdf/graphs-fpgas-survey.pdf
(submitted to arXiv, will appear tonight)

## Slide 6
Vertex-centric, Gather-Apply-Scatter, ... ?
[1] S. Salihoglu and J. Widom, “Optimizing graph algorithms on Pregel-like systems”. VLDB. 2014.
“(...) implementing graph algorithms efﬁciently on Pregel-like systems (...) can be surprisingly difﬁcult and require careful optimizations.” [1]
+ other issues
What programming paradigm and why?
To be able to utilize pipelining well, we really want to use streaming (aka edge-centric)

## Slide 7
Streaming all edges in and out is one “pass”. Repeat it a certain (algorithm-dependent) number of times
…How to minimize the number of “passes” over edges? This can get really bad in the “traditional” edge-centric approach (e.g., BFS needs D passes; D = diameter [1]).
What programming paradigm and why?
[1] A. Roy et al. X-stream: Edge-Centric Graph Processing using Streaming Partitions. SOSP. 2013.
DRAM
Some processing unit (CPU, GPU, FPGA, …, for a moment we don’t care)
Use some form of streaming (aka edge-centric); we can use pipelining efficiently (“streaming ≈ pipelining”)
…Processing edges is sequential – how to incorporate parallelism?
Issues…

## Slide 8: Substream-Centric Graph Processing
Part 2: A new paradigm for processing graphs
It enhances edge-centric streaming approaches
…
Divide the input stream of edges according to some (algorithm-specific) pattern
Process “substreams” independently
Merge substreams
What programming paradigm and why?
DRAM
Also, it enables (tunable) approximation and a (tunable) number of passes
Use some form of streaming (aka edge-centric); we can use pipelining efficiently (“streaming ≈ pipelining”)
…Processing edges is sequential – how to incorporate parallelism?
Substreams (pipelines) are processed in parallel, in a simple way (independently, except for merging)
Part 2: Substream-Centric: A new paradigm for processing graphs
Weighted edges
How to express MWM in this paradigm?

## Slide 9: Research Questions
Which programming paradigm to use for (approximate) MWM
(and many other problems)?
How to design a high-performance MWM algorithm (as dictated by the used paradigm)?
What is the HW FPGA design that ensures high performance?
What is the ultimate performance, power consumption, and the related tradeoffs?
Use substream-centric processing (exposes parallelism, enables easy pipelining, supports approximation)

## Slide 10
Part 3: Analysis of models and algorithms for streaming graph processing
~30 algorithms for streaming (approximate) MWM
Maximize accuracy
Most important
goals:
Minimize local space
Minimize #passes
Expose parallelism (match substream-centric)
Part 3: Analysis of models and algorithms for streaming graph processing
Crouch and Stubbs [1]
No worries, no need to analyze it here, all the details are in the paper 
Idea: let’s check the (rich) world of streaming theory and see if there is anything out there that we could use 

## Slide 11: Substream-Centric Graph Processing
…
How to minimize the number of “passes”?
Select edges with weights:
Greedy merge of matchings into the final MWM
Edges are streamed only once!
Substream 0
Substream L-1
Substream i
The algorithm is (4+ε)-approximation, but we’ll show in practice it does not matter much
Compute unweighted matchings separately
[1] M. Crouch and D. M. Stubbs. Improved streaming Algorithms for weighted Matching, via unweighted Matching. LIPIcs-Leibniz Informatics. 2014.
+ Crouch and Stubbs MWM [1]
A parameter that controls accuracy
DRAM

## Slide 12: Substream-Centric Graph Processing
FPGA
Time: O(m)
Work: O(Lm)
CPU
Time: O(Ln)
Work: O(Ln)
Use a hybrid CPU-FPGA setting!
…
How to minimize the number of “passes”?
Edges are streamed only once!
Substream 0
Substream L-1
Substream i
The algorithm is (4+ε)-approximation, but we’ll show in practice it does not matter much
[1] M. Crouch and D. M. Stubbs. Improved streaming Algorithms for weighted Matching, via unweighted Matching. LIPIcs-Leibniz Informatics. 2014.
+ Crouch and Stubbs MWM [1]
DRAM
Part 4: Mapping the algorithm to the „right” hardware configuration
Pipelines – it fits FPGA well!
Inherently sequential – it fits CPU well

## Slide 13: Substream-Centric Graph Processing
FPGA
Time: O(m)
Work: O(Lm)
CPU
Time: O(Ln)
Work: O(Ln)
Use a hybrid CPU-FPGA setting!
…
How to minimize the number of “passes”?
Edges are streamed only once!
Substream 0
Substream L-1
Substream i
The algorithm is (4+ε)-approximation, but we’ll show in practice it does not matter much
[1] M. Crouch and D. M. Stubbs. Improved streaming Algorithms for weighted Matching, via unweighted Matching. LIPIcs-Leibniz Informatics. 2014.
+ Crouch and Stubbs MWM [1]
DRAM
Part 5: Implementing all of this on the FPGA-CPU platform

## Slide 14: Substream-Centric Graph Processing
FPGA
Time: O(m)
Work: O(Lm)
CPU
Time: O(Ln)
Work: O(Ln)
Use a hybrid CPU-FPGA setting!
…
How to minimize the number of “passes”?
Edges are streamed only once!
Substream 0
Substream L-1
Substream i
The algorithm is (4+ε)-approximation, but we’ll show in practice it does not matter much
[1] M. Crouch and D. M. Stubbs. Improved streaming Algorithms for weighted Matching, via unweighted Matching. LIPIcs-Leibniz Informatics. 2014.
+ Crouch and Stubbs MWM [1]
DRAM

## Slide 15: Substream-Centric MWM: FPGA optimizations
Vectorization
Blocking
Pipelining
Prefetching
They are often used in graph processing schemes on FPGAs; we apply them as well.
(related mostly to matching bits)

## Slide 16: Substream-Centric MWM: FPGA optimizations
All the details are in the paper. Let’s focus on the key FPGA design ideas and optimizations
Vectorization
Blocking
Pipelining
Prefetching
They are often used in graph processing schemes on FPGAs; we apply them as well.

## Slide 17: Substream-Centric MWM: FPGA optimizations
Edge reordering on the fly (more details in a bit)
Parallel substreams
Blocking (more details in a bit)
Vectorization
Blocking
Pipelining
Prefetching
They are often used in graph processing schemes on FPGAs; we apply them as well.
All the details are in the paper. Let’s focus on the key FPGA design ideas and optimizations

## Slide 18: Substream-Centric MWM: FPGA optimizations Blocking
Adjacency Matrix
An edge between vertices 0 and 1
An edge between vertices 0 and 2
depends on
depends on
depends on
depends on
depends on
Stalling between every row needed...
Introduce a (tunable) „blocking parameter” K
K determines how many stalls are allowed
K = 3
Row IDs correspond to vertex IDs
Column IDs correspond to vertex IDs
0
1
2
3
4
5
0
1
2
3
4
5
Notes: Lets take a closer look at the vectorization. Remember how we were able to compute a maximal matching by a simple bit array. In this example shown here, we compute 5 maximal matchings in parallel.
So first of all, we load an edge from main memory to the FPGA. Assume we are therefore given some edge e with vertices u, v, and edge weight w.
We then load two vectors from main memory to the FPGA. A vector tells us if u or v is already a part of a matching. If we would compute only one matching, the vector would have 1 entry, as seen at the beginning. But since we compute 5 maximal matchings at once, we need 5 entries per vertex. The values we have chosen here are just for demonstration.
We now need to decide, if this edge is part of a substream. This decision is made by comparing the edge’s weight to constant values, which depend on epsilon. Overall, we need to compute L many integer comparisons.
We then decide, if we can add an edge to a maximal matching. This is done element-wise, by considering the loaded vector and the decision, if the edge is part of the substream. We can add the edge to the matching, if the according entries in the loaded vector are 0, and e is part of the substream. Otherwise, the edge is not added. In this example here, we cannot add the edge to the matching, since there is already an incident edge to vertex u.
Finally, we update the vectors and write them back to main memory, and add the edge to the appropriate matchings.

## Slide 19: Substream-Centric MWM: FPGA optimizations Blocking
Adjacency Matrix
Introduce a (tunable) „blocking parameter” K
K determines how many stalls are allowed
Portions of rows are ordered „lexicographically” (i.e., no strict ordering that enforces a stall is required)
Algorithm still (provably) correct
depends on
K = 3
K is tunable: it controls the tradeoff between the amount of the used FPGA resources and the performance
Notes: Lets take a closer look at the vectorization. Remember how we were able to compute a maximal matching by a simple bit array. In this example shown here, we compute 5 maximal matchings in parallel.
So first of all, we load an edge from main memory to the FPGA. Assume we are therefore given some edge e with vertices u, v, and edge weight w.
We then load two vectors from main memory to the FPGA. A vector tells us if u or v is already a part of a matching. If we would compute only one matching, the vector would have 1 entry, as seen at the beginning. But since we compute 5 maximal matchings at once, we need 5 entries per vertex. The values we have chosen here are just for demonstration.
We now need to decide, if this edge is part of a substream. This decision is made by comparing the edge’s weight to constant values, which depend on epsilon. Overall, we need to compute L many integer comparisons.
We then decide, if we can add an edge to a maximal matching. This is done element-wise, by considering the loaded vector and the decision, if the edge is part of the substream. We can add the edge to the matching, if the according entries in the loaded vector are 0, and e is part of the substream. Otherwise, the edge is not added. In this example here, we cannot add the edge to the matching, since there is already an incident edge to vertex u.
Finally, we update the vectors and write them back to main memory, and add the edge to the appropriate matchings.

## Slide 20: Research Questions
Which programming paradigm to use for (approximate) MWM
(and many other problems)?
How to design a high-performance MWM algorithm (as dictated by the used paradigm)?
What is the HW FPGA design that ensures high performance?
What is the ultimate performance, power consumption, and the related tradeoffs?
The proper use of blocking, vectorization, pipelining, prefetching
Use substream-centric processing (exposes parallelism, enables easy pipelining, supports approximation)
Combine the MWM algorithm by Crouch and Stubbs with a hybrid CPU-FPGA setting

## Slide 21
Performance Analysis
Types of machines
CPU: Intel Broadwell
Xeon E5-2680 v4 @3.3 GHz
14 Cores (28 Threads)
Altera Arria 10 @200MHz
Part 6: Evaluation
Notes: The Interlagos processor is viewed by the Linux operating system in /proc/cpuinfo as having 16 "processors" per chip. These "processors" are the schedualable integer cores

## Slide 22
Performance Analysis
Types of graphs
Real-world graphs (SNAP [2], KONECT [3], DIMACS [4])
Synthetic graphs
Kronecker [1]
[1] J. Leskovec et al. Kronecker Graphs: An Approach to Modeling Networks. J. Mach. Learn. Research. 2010.
[2] SNAP. https://snap.stanford.edu
Road networks
Communication graphs
Social networks
Purchase networks
Citation graphs
Web graphs
[3] KONECT. https://konect.cc
[4] DIMACS Challenge

## Slide 23
Performance Analysis
Algorithms
Our FPGA design, (4+ε)-approximation
CPU implementations of the original Crouch scheme, (4+ε)-approximation
We test both CPU and hybrid (FPGA+CPU) platforms
[1] M. Crouch and D. M. Stubbs. Improved streaming Algorithms for weighted Matching, via unweighted Matching. LIPIcs-Leibniz Informatics. 2014.
[2] M. Ghaffari. Space-optimal semi-streaming for(2+ε)-approximatematching. arXiv:1701.03730, 2017.
State-of-the-art MWM algorithm, space-optimal, time-optimal (O(m)), (2+ε)-approximation

## Slide 24
SC-OPT secures highest performance
Performance Analysis
Various Graphs
Parameters:
Blocking size (K) = 32, #Substreams (L) = 64
#Threads = 4, ε = 0.1
Hybrid
Hybrid
CPU
CPU

## Slide 25
SC-OPT is comparable to the (2+ε)-approximation by Ghaffari et al.
Performance Analysis
Approximation (Accuracy)
Parameters:
#Substreams (L) = 128, Blocking size (K) = 32, #threads = 4, #edges = 8M (Kronecker)

## Slide 26
SC-OPT (Hybrid) is ~8x more power-efficient than the CPU implementation
Performance Analysis
Energy Consumption, Resource Utilization
Blocking needs more resources (but is tunable!)
Parameters:
L: #Substreams (pipelines),
K: Blocking size,
T: #CPU threads

## Slide 27
Addition complexity grows linearly with L
Performance Analysis
Design Space Exploration
BRAM signal propagation limits the frequency
B – BRAM size allocated for matching data structures,
L – number of substreams (pipelines)

## Slide 28: Other Algorithms, Problems, Analyses
In addition to MWM, we also analyzed more graph problems
Triangle counting
Connected components
Minimum spanning trees
Triangle counting
Colorings
Connectivity
K-edge connectivity
K-vertex connectivity
Bipartiteness
Sparsification
Spanners
Random walks
Motif counting
Densest subgraphs
Work in progress on the distributed setting 
Again, the most relevant parts are in the FPGA paper, the rest in this survey (ready in ~1-2 months)
To enable rigorous reasoning, we analyzed ~15 models for streaming graph processing (and selected the best for FPGAs)
StreamSort
Vertex-arrival
W-Stream
Sliding window
Semi-streaming
Cash-register
Dynamic
Adjacency-list
Simple streaming
Annotated streaming
Insert-only
Turnstile
Online
MapReduce
Graph Sketching
MUD
http://spcl.inf.ethz.ch/Publications/.pdf/graphs-fpgas-survey.pdf
(submitted to arXiv, will appear tonight)
Notes: - Where is the promised case study?

## Slide 29
Substream-Centric graph processing paradigm, exposes parallelism, enables easy pipelining, supports approximation
Detailed domain analysis,
identification of Semi-Streaming Model as FPGA best-fit, 2 surveys
Generic FPGA design, code available
Theory-inspired MWM approximate algorithm
on a hybrid CPU-FPGA setting
Generalizability to other graph problems and settings
Thank you
for your attention
Website & code: http://spcl.inf.ethz.ch/Research/Parallel_Programming/Substream-Centric
Notes: - Where is the promised case study?

## Slide 30
BACKUP & EXTENTED SLIDES
Notes: - Where is the promised case study?

## Slide 31: Large graphs…
[1] A. Roy et al. X-stream: Edge-Centric Graph Processing using Streaming Partitions. ACM Symposium on Operating Syst. 2013.
[2] S. Zhou et al. High-throughput and Energy-efficient Graph Processing on FPGA. FCCM. 2016.
Problems?
Irregular
Data-driven
Communication- and synchronization-heavy
Low power efficiency!
250 Watts
Graph Problem | CPU (MTEPS/Watt) [1] | FPGA (MTEPS/Watt) [2]
SSSP | 1.9 | 30.2
CC | 0.5 | 48.1
MST | 0.6 | 44.3
120 Watts
Let’s use FPGAs for Maximum Matchings...

## Slide 32: Large graphs…
Irregular
Data-driven
Communication- and synchronization-heavy
250 Watts
120 Watts

## Slide 33: Large graphs…
Why do we care?
Social networks
Engineering networks
Useful model
Biological networks
Physics, chemistry
Communication networks
...even philosophy 
Machine learning
Collaborator experience?
Disease spread channels?
Terrorism prevention?
Most relevant protein?
Gene alignment?
Brain structure?
Best phone connection?
Least expensive computer network?
Shortest network path?
Most efficient road network?
Most reliable grid network?
Shortest
path?

## Slide 34
What programming paradigm and why?
7 paradigms
Part 1: To understand the domain well, we conducted a detailed analysis of graph processing on FPGAs
Key techniques, challenges, features, …
Selected MWM-related parts are in the FPGA paper, the rest is in…
What are the most promising techniques?
~25 FPGA accelerators for specific algorithms
~15 FPGA graph processing frameworks
Part 1: To understand the domain well, we conducted a detailed analysis of graph processing on FPGAs
https://arxiv.org/abs/...

## Slide 35
Vertex-centric, Gather-Apply-Scatter, ... ?
Well...
Assumes the whole input graph is accessible…
It was designed with the “batch” analytics in mind.
…when in BRAM, size is severely limited
…when in DRAM, accessing & pipelining become complex
[1] S. Salihoglu and J. Widom, “Optimizing graph algorithms on Pregel-like systems”. VLDB. 2014.
“(...) implementing graph algorithms efﬁciently on Pregel-like systems (...) can be surprisingly difﬁcult and require careful optimizations.” [1]
What programming paradigm and why?
Vertex-Centric (aka Pregel-like) approach is complex for problems such as matchings, spanning trees, etc.

## Slide 36
Vertex-centric, Gather-Apply-Scatter, ... ?
It was designed with the “batch” analytics in mind.
It assumes the whole input is accesible. When in DRAM, accessing & pipelining becomes complex.
[1] S. Salihoglu and J. Widom, “Optimizing graph algorithms on Pregel-like systems”. VLDB. 2014.
“(...) implementing graph algorithms efﬁciently on Pregel-like systems (...) can be surprisingly difﬁcult and require careful optimizations.” [1]
What programming paradigm and why?
Vertex-Centric (aka Pregel-like) approach is complex for problems such as matchings, spanning trees, etc.
To be able to utilize pipelining well, we really want to use streaming (aka the edge-centric paradigm)

## Slide 37
Well...
Assumes the whole input graph is accessible…
Can be used but it was designed with the “batch” analytics in mind
…when in DRAM, accessing & parallelization become complex
KONECT graph datasets
Webgraph datasets
Vertex-centric, Gather-Apply-Scatter, ... ?
What programming paradigm and why?
Huge
…when in BRAM, size is severely limited

## Slide 38
Processing edges is sequential – how to incorporate parallelism?
DRAM
Some processing unit (CPU, GPU, FPGA, …)
Repeat certain (algorithm-dependent) number of times
How to minimize the number of “passes” over edges? (This can get really bad in the “traditional” edge-centric approach, e.g., BFS normally needs O(m+n) work, while in the edge-centric approach it takes O(D m) work (D passes [1]),
How to implement efficiently on an FPGA?
What programming paradigm and why?
[1] A. Roy et al. X-stream: Edge-Centric Graph Processing using Streaming Partitions. SOSP. 2013.
m: #edges in a graph
n: #vertices in a graph
D: graph’s diameter
(usually ~5-15)
Use some form of streaming (aka edge-centric)

## Slide 39
Hundreds of papers and schemes, how to select a “streaming model” or an algorithm to use? 
~30 algorithms for streaming (approximate) MWM
~15 models for streaming graph processing
We investigated the vast majority of cases, and… guess what happened 
It is almost ready (may take ~1 month more) – if you want to check it out earlier, let us know!
Which one to select?
Any interesting idea to use
in the context of FPGAs and substream-centric processing?
We analyzed…

## Slide 40
Part 3: Analysis of models and algorithms for streaming graph processing
~15 models for streaming graph processing
Which one to select?
Using a model enables rigorous analysis of the algorithm behavior
Selecting a right model enables more realistic predictions about the algorithm behavior on given hardware
Limiting oneself to a particular model helps to select the best algorithm or technique (within that model)
Why even should we care?
Part 3: Analysis of models and algorithms for streaming graph processing

## Slide 41
StreamSort
Vertex-arrival
W-Stream
Sliding window
Semi-streaming
Cash-register
Dynamic
Adjacency-list
Simple streaming
Annotated streaming
Insert-only
Turnstile
Online
MapReduce
Graph Sketching
MUD
~15 models for streaming graph processing
Which one to select?
To understand the models (and related caveats) well, we developed a formal taxonomy of the analyzed models with the aim of guiding future graph streaming designs (check the report for details  )

## Slide 42
Semi-streaming [1]
Covers a general streaming setting (= works for substream-centric)
Offers (potentially powerful) MWM algorithms
Assumes O(n logc n) local space that can be used for processing an edge  fits well FPGA BRAM constraints!
Why semi-streaming, and what does it mean?
[1] J. Feigenbaum et al. On graph problems in a semi-streaming model. Theoretical CS, 2005

## Slide 43: Research Questions
Which programming paradigm to use for (approximate) MWM?
How to design a high-performance MWM algorithm (as dictated by the used paradigm)?
What is the HW FPGA design that ensures high performance?
What is the ultimate performance, power consumption, and the related tradeoffs?
Use substream-centric processing (exposes parallelism)
For enabling theoretical analysis and rigor in the context of FPGAs (small local space), use the semi-streaming model

## Slide 44
Part 3 continued : Analysis of models and algorithms for streaming graph processing
~30 algorithms for streaming (approximate) MWM (in the semi-streaming model)
Any interesting idea to use
in the context of FPGAs and substream-centric processing?
Maximize accuracy
Our
goals:
Minimize local space
Minimize #passes
Accept weighted graphs
Expose parallelism (match substream-centric)
Accept general (not just bipartite) graphs
Part 3 continued: Analysis of models and algorithms for streaming graph processing
More specifically...
Part 3 continued: Analysis of models and algorithms for streaming graph processing

## Slide 45: Research Questions
Which programming paradigm to use for (approximate) MWM
(and many other problems)?
How to design a high-performance MWM algorithm (as dictated by the used paradigm)?
What is the HW FPGA design that ensures high performance?
What is the ultimate performance, power consumption, and the related tradeoffs?
Use substream-centric processing (exposes parallelism)
Use the MWM algorithm by Crouch and Stubbs in the substream-centric paradigm in a hybrid CPU-FPGA setting
For enabling theoretical analysis and rigor in the context of FPGAs (small local space), use the semi-streaming model

## Slide 46: Substream-Centric MWM: FPGA optimizations
No, we will not analyze this now  All the details are in the paper. Let’s focus on the key FPGA design ideas and optimizations
Vectorization
Blocking / Tiling
Pipelining
Prefetching
They are often used in graph processing schemes on FPGAs; we apply them as well.

## Slide 47
The Space of Substream-Centric
Amount of FPGA resources
Accuracy
Locality vs fairness (for writers)
Design A
Design B
Notes: Writers don’t run wildly: we structure them inside small MCS queues
Ask patrick about the exact semantics of b|x|y. Can it be NOT exact?
T_L,i ? Think about it...

## Slide 48: Research Questions
Which programming paradigm to use for (approximate) MWM?
How to design a high-performance MWM algorithm (as dictated by the used paradigm)?
What is the HW FPGA design that ensures high performance?
What is the ultimate performance, power consumption, and the related tradeoffs?
Use substream-centric processing (exposes parallelism)
The proper use of blocking, vectorization, and others (pipelining, prefetching)
For enabling theoretical analysis and rigor in the context of FPGAs (small local space), use the semi-streaming model
Use the MWM algorithm by Crouch and Stubbs in the substream-centric paradigm in a hybrid CPU-FPGA setting

## Slide 49
SC-OPT secures highest performance
Performance Analysis
Various Graphs
Parameters:
Blocking size = 32, #Substreams = 64
#Threads = 4, ε = 0.1
Hybrid
Hybrid
CPU
CPU

## Slide 50
SC-OPT secures highest performance for all considered numbers of threads
Performance Analysis
Various Thread (CPU) Counts
Blocking size = 32, #Substreams = 64
#edges = 16M (Kronecker), ε = 0.1

## Slide 51
SC-OPT secures highest performance for all considered values of parameters
Performance Analysis
Various blocking size (K) and #substreams (L)
Blocking size (K) = 32, #threads = 4,
#edges = 16M (Kronecker), ε = 0.1
#Substreams (L) = 128, #threads = 4,
#edges = 16M (Kronecker), ε = 0.1

## Slide 52
SC-OPT is comparable to the (2+ε)-approximation by Ghaffari et al.
Performance Analysis
Approximation
Blocking size (K) = 32, #threads = 4,
#Substreams (L) = 128 , ε = 0.1
#Substreams (L) = 128, Blocking size (K) = 32, #threads = 4, #edges = 8M (Kronecker)

## Slide 53: Other Algorithms, Problems, Analyses
Well, not enough time to present 
In addition to MWM, we also analyzed many more graph problems
Triangle counting
Connected components
Minimum spanning trees
Triangle counting
Colorings
Connectivity
K-edge connectivity
K-vertex connectivity
Bipartiteness
Cut sparsification
Spectral sparsification
Spanners
Random walks
Motif counting
Densest subgraphs
Preliminary substream-centric designs and results
Work in progress on the distributed setting 
Again, the most relevant parts are in the FPGA paper, the rest in this survey (ready in ~1-2 months)
 https://arxiv.org/abs/...
Notes: - Where is the promised case study?

## Slide 54: Substream-Centric MWM: FPGA design

## Slide 55
Matching Bits: Key Data Structures for Maintaining Information on Matchings
1
0
1
0
0
0
0
0
0
0
e = (u, v, weight)
L „row” bit vectors (one
per substream)
...
An incoming edge...
n „column” bit vectors (one per vertex)
Vertex u is a part of a matching in substreams 0, 2
u-th vector
v-th vector
Vertex v is not a part of any matching
(L = 5)
1
0
1
0
0
L bits (one per substream)
For the current edge, is...
(L = 5)
Vertices + matchings (correctness)
Edges + matchings (more performance)
weight ?
weight ?
weight ?
weight ?
weight ?
Notes: Lets take a closer look at the vectorization. Remember how we were able to compute a maximal matching by a simple bit array. In this example shown here, we compute 5 maximal matchings in parallel.
So first of all, we load an edge from main memory to the FPGA. Assume we are therefore given some edge e with vertices u, v, and edge weight w.
We then load two vectors from main memory to the FPGA. A vector tells us if u or v is already a part of a matching. If we would compute only one matching, the vector would have 1 entry, as seen at the beginning. But since we compute 5 maximal matchings at once, we need 5 entries per vertex. The values we have chosen here are just for demonstration.
We now need to decide, if this edge is part of a substream. This decision is made by comparing the edge’s weight to constant values, which depend on epsilon. Overall, we need to compute L many integer comparisons.
We then decide, if we can add an edge to a maximal matching. This is done element-wise, by considering the loaded vector and the decision, if the edge is part of the substream. We can add the edge to the matching, if the according entries in the loaded vector are 0, and e is part of the substream. Otherwise, the edge is not added. In this example here, we cannot add the edge to the matching, since there is already an incident edge to vertex u.
Finally, we update the vectors and write them back to main memory, and add the edge to the appropriate matchings.

## Slide 56
SC-OPT secures highest performance for all considered values of parameters
Performance Analysis
Various #substreams (L)
Parameters:
Blocking size (K) = 32, #threads = 4,
#edges = 16M (Kronecker), ε = 0.1
#Substreams (pipelines)
Hybrid
CPU

## Slide 57: Large graphs…
Communication- and synchronization-heavy
250 Watts
120 Watts