## Slide 1
Cloud-DNN: An Open Framework for Mapping DNN Models to Cloud FPGAs
Yao Chen1, Jiong He1, Xiaofan Zhang2, Cong Hao2, Deming Chen1,2
1Advanced Digital Sciences Center, Singapore
2 University of Illinois at Urbana-Champaign, IL, USA

## Slide 2: Outline
Background, challenges and motivation
Cloud-DNN overview
Synthesizable library design
System architecture generation
Cloud-DNN framework in detail
Evaluations
Conclusion and future work

## Slide 3: Background
DNNs are driving the next-generation AI revolution
  A lot of applications are latency sensitive
  DNNs are computationally intensive
CPU/GPU are commonly used and easy to program
  CPUs may not deliver the required performance
  GPUs are very power hungry
ASIC can deliver high performance and energy efficiency
  Long time to market
  Less flexibility
FPGAs
  Low latency, energy-efficient and re-configurable platform for both cloud and embedded scenarios
  Hard to program

## Slide 4: Background: FPGA in the cloud
High-Definition Pictures/videos
Streaming Input
Big Data Volume
Implementation constraints: e.g., memory, logic resource

## Slide 5: Challenges and our solutions
Difficult to program targeting high performance and fast deployment
Our solution: parameterized C++ template library for high
performance accelerator IP generation, HLS optimizations
Difficult to implement without timing violation
Difficult to support both hardware and software
Our solution: split to sub-nets with architectural consideration
Our solution: APIs for accelerator control, software generation
HLS implementation
& Optimization

## Slide 6: Cloud-DNN: An Open-Source Framework targeting Cloud-FPGA
Synthesizable function library
Automated generation flow
DSE for optimization
API and call function generation
Our Tool Chain
DNN models
Cloud implementation
Optimized for performance
Suitable for HLS design flow
Avoid tedious hardware programming and verification
Optimal hardware configuration exploration
System level solution for DNN applications

## Slide 7: Outline
Background, challenges and motivation
Cloud-DNN overview
Synthesizable library design
System architecture generation
Cloud-DNN framework in detail
Evaluations
Conclusion and future work

## Slide 8: Cloud-DNN Overview
Extract
Analyze
Generate
Implementation

## Slide 9: Cloud-DNN Overview
Extract
Analyze
Generate
Implementation
(1) Synthesizable library
(2) System architecture
(3) Generation flow

## Slide 10: Outline
Background, challenges and motivation
Cloud-DNN overview
Synthesizable library design
System architecture generation
Cloud-DNN framework in detail
Evaluations
Conclusion and future work

## Slide 11: Layer function IPs
CONV_1
ReLU_1
Tensor-to-Tensor (TT) | Element-wise (EW)
Conv | ReLU
Pooling | Sigmoid
InnerProduct | Tanh
DeConv | BN
…… | …..
POOL_1
FC_1

## Slide 12: Layer accelerator template
C++ template class
Easily configured with template parameters
Fully synthesizable and flexible
Element-wise function as in-line functions
Tensor-to-tensor functions are layer templates

## Slide 13: Sub-net template
Die0
Die1
Die2

## Slide 14: Synthesizable library
Template class and parameters
Conv_acc<DataType, Tm_0, Tn_0, Tr_0, Tc_0> convAcc0;
Conv_acc<DataType, Tm_1, Tn_1, Tr_1, Tc_1> convAcc1;
Pool_acc< …..
Examples:

## Slide 15: Accelerator models
Performance model
Convolution
Pooling
Resource model
*

## Slide 16: Outline
Background, challenges and motivation
Cloud-DNN overview
Synthesizable library design
System architecture generation
Cloud-DNN framework in detail
Evaluations
Conclusion and future work

## Slide 17: System architecture generation
One sub-net per die
Controllable connection between dies during system generation
Shell integration
DMA enabled
Physical constraints to allocate the modules to different locations

## Slide 18: API function support
Host processor manage accelerator status
Application ignores the hardware detail
Necessary data movement functions
Implemented as light weighted functions

## Slide 19: Outline
Background, challenges and motivation
Cloud-DNN overview
Synthesizable library design
System architecture generation
Cloud-DNN framework in detail
Evaluations
Conclusion and future work

## Slide 20: Cloud-DNN in detail
Configuration file
Acc_num
Acc_type
Acc_parameters

## Slide 21: Outline
Background, challenges and motivation
Cloud-DNN overview
Synthesizable library design
System architecture generation
Cloud-DNN framework in detail
Evaluations
Conclusion and future work

## Slide 22: Evaluations
Experimental setup:
Local cloud: UltraScale+ VU118 platform (Xilinx VU9P FPGA chip)
AWS cloud: F1.2Xlarge instance (Xilinx VU9P FPGA chip)
Resource evaluation
Logic | BRAM | DSP48 | URAM
2585K | 75.9Mb | 6840 | 270Mb
Sub-net_0

## Slide 23: Comparison with Software Implementation
2.18X faster than GPU
104X faster than CPU
CPU platform: E5-2430 with 32GB DDR
GPU platform: E5-2609 + Pascal Titan X GPU

## Slide 24: Evaluations
[5] Jiantao Qiu et al. Going deeper with embedded FPGA platform for convolutional neural network. In Proc. of FPGA, 2016.
[20] Chen Zhang et al. Optimizing FPGA-based accelerator design for deep convolutional neural networks. In FPGA, 2015.
[26] Chen Zhang et al. Caffeine: towards uniformed representation and acceleration for deep convolutional neural networks. In Proc. of ICCAD, 2016.
[27] Yijin Guan et al. FP-DNN: An automated framework for mapping deep neural networks onto FPGAs with RTL-HLS hybrid templates. In Proc. of FCCM, 2017.
[28] Yufei Ma et al. An automatic RTL compiler for high-throughput FPGA implementation of diverse deep convolutional neural networks. In Prof. of FPL, 2017.
Comparison with other designs
1.6X
6.6X
1.5X
1.5X
2.7X
11.2X
2.6X
2.5X

## Slide 25: Outline
Background, challenges and motivation
Cloud-DNN overview
Synthesizable library design
System architecture generation
Cloud-DNN framework in detail
Evaluations
Conclusion and future work

## Slide 26: Conclusion & Future work
Conclusion
  Open-source framework, including synthesizable layer function library, automated structural optimization and code generation
  More energy efficient solution than others
  Fast development of high-performance, power efficient on-cloud DNN acceleration system
Future work
  More functional support (eg, RNN)
  Performance enhancement
  More framework support, TensorFlow, MxNet, etc.
  Extension of design methodology, RTL-HLS hybrid, etc.
  https://github.com/microideax/Open-Dnn.git

## Slide 27: Thank you!
Q&A