## Slide 1
LANMC: LSTM-Assisted Non-Rigid Motion Correction
on FPGA for Calcium Image Stabilization
Zhe Chen1, Hugh T. Blair2, Jason Cong1
1Computer Science Department, 2Department of Psychology, UCLA
zhechen@ucla.edu

## Slide 2: Research Background
[1] Denise J. Cai, Daniel Aharoni et al., Nature, 2016
Non-uniform motion artifacts
Costly and Low Efficient Algorithm
Real-Time Non-Rigid motion correction for calcium imaging IN DEMAND.
Motivation
Miniscope Calcium Imaging [1] Monitoring neuron activities at large scale in vivo.
Challenge
Notes: Miniscope Calcium Imaging [1] Monitoring neuron activities at large scale in vivo.

## Slide 3: Conventional Non-Rigid Motion Correction Method
2D Contrast Filter
Remove the bulk of background
Filter size: Cell diameter in image
Piecewise Rigid Motion Correction
Divide overlapping patches
Cross correlation based on FFT/IFFT
Local Maximum -> Motion Vector
Processing Steps
The operation needs to be repeated for each single patch.
It causes algorithm to be costly and inefficient for real-time application.
Algorithm Inefficiency:

## Slide 4: Proposed Method based on LSTM Inference
METHOD: Use long short-term memory (LSTM) inference to predict motion at overlap patches
Accuracy Evaluation:
Offline Training
NoRMCorre -> Get training target
Online Inference
Rigid motion correction + LSTM Inference
95% operation is saved by using 5-node LSTM

## Slide 5: Implementation: Folding Architecture
Leverage the central symmetry of the filter kernel with Folding
I0
I1
I2
I3
I4
C0
C1
C2
C1
C0
Save >80% LUT, FF and >60% DSP compared to design w/o folding
Performance Evaluation
 | Frequency (MHz) | Runtime (ms)
Zynq-7045 | 100 | 3.73
Zynq-7045 | 300 | 1.25
CPU w/ 4T | 1.2-1.5 GHz | 134.6
CPU w/ 8T | 1.2-1.5 GHz | 89.7
CPU w/ 16T | 1.2-1.5 GHz | 61.9
At 300 MHz, FPGA achieves >40x speedup over the CPU

## Slide 6: Implementation: Reuse FFT/IFFT and LSTM
Unroll and Pipeline FFT/IFFT Operation
Reuse FFT/IFFT IP for H/V Transformation
Unroll and Pipeline LSTM Inference Acceleration
Reuse LSTM for H/V Direction and All Patches
Vivado HLS

## Slide 7: Performance Evaluation
Conclusion
FPGA design realizes real-time non-rigid motion correction for calcium image.
Low latency and high energy efficiency suitable for closed-loop feedback stimulation.
Simplify algorithm by LSTM inference
Consistent speedup of acceleration kernels
Low power high efficient Ultra96 board
Processing Latency
Energy Efficiency
compared to Xeon E52620 CPU
82x Speedup
Close to 4 orders Gain

## Slide 8: Thank you!
Acknowledgments