## Slide 1: HeteroCL: A Multi-Paradigm Programming Infrastructure for Software-Defined Reconfigurable Computing
Yi-Hsiang Lai1, Yuze Chi2, Yuwei Hu1, Jie Wang2, Cody Hao Yu2,3,
Yuan Zhou1, Jason Cong2, Zhiru Zhang1
1Cornell University
2University of California, Los Angeles
3Falcon Computing Solutions, Inc.

## Slide 2: Essential Techniques for Hardware Acceleration
Compute customization
Parallelization
Pipelining, etc.
Data type customization
Low-bitwidth integer
Fixed point, etc.
Memory customization
Banking
Data reuse, etc
There exists interdependence among different customizations
+
32
+
32
+
32
...
+
32
+
32
...
+
+
16
+
8
+
8
+
4
...
+
16
+
...
+
mem
mem
FIFO
FIFO
...
...
mem

## Slide 3: Hardware Customization in High-Level Synthesis
Custom memory
(Reuse buffers)
Driving example: convolutional kernel
for (int y = 0; y < N; y++)
for (int x = 0; x < N; x++)
for (int r = 0; r < 3; r++)
for (int c = 0; c < 3; c++)
out[x, y] += image[x+r, y+c] * kernel[r, c]
Custom compute
(Loop tiling)
Custom data type
(Quantization)
#pragma HLS array_partition variable=filter dim=0
hls::LineBuffer<3, N, ap_fixed<8,4> > buf;
hls::Window<3, 3, ap_fixed<8,4> > window;
for(int y = 0; y < N; y++) {
for(int xo = 0; xo < N/M; xo++) {
#pragma HLS pipeline II=1
for(int xi = 0; xi < M; xi++) {
int x = xo*M + xi;
ap_fixed<8,4> acc = 0;
ap_fixed<8,4> in = image[y][x];
buf.shift_up(x);
buf.insert_top(in, x);
window.shift_left();
for(int r = 0; r < 2; r++)
window.insert(buf.getval(r,x), i, 2);
window.insert(in, 2, 2);
if (y >= 2 && x >= 2) {
for(int r = 0; r < 3; r++) {
for(int c = 0; c < 3; c++) {
acc += window.getval(r,c) * kernel[r][c];
}}
out[y-2][x-2] = acc;
}}}}
Algorithm#1
Compute Customization
Algorithm#2
Data Type Customization
Memory Customization
Algorithm#3
Entangled hardware customization and algorithm
Less portable
Less maintainable
Less productive

## Slide 4: Decoupling Algorithm from Hardware Customization
Algorithm#1,2,3
Compute Customization
Data Type Customization
Memory Customization
Algorithm#1
Compute Customization
Algorithm#2
Data Type Customization
Memory Customization
Algorithm#3
HLS C
HeteroCL
Algorithm#1,2
Data Type Customization
Memory Customization
Algorithm#3
Compute Customization
Memory Customization
Halide, TVM, etc.
Entangled algorithm specification and customization schemes [1,2,3]
Decoupled temporal schedules [4,5,6,7,8]
Fully decoupled customization schemes +
Clean abstraction capturing the interdependence
[1] Intel HLS
[2] Xilinx Vivado HLS
[3] Canis, et al. FPGA’11
[4] Ragan-Kelly, et al. SIGPLAN’13
[5] Baghdadi, et al. arXiv’18
[6] Rong, et al. arXiv’17
[7] Pu, et al. TACO’17
[8] Chen, et al. arXiv’18

## Slide 5: Decoupled Compute Customization
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))
HeteroCL code
HLS code
for (int y = 0; y < N; y++)
for (int x = 0; x < N; x++)
for (int r = 0; r < 3; r++)
for (int c = 0; c < 3; c++)
out[x, y] += image[x+r, y+c] * kernel[r, c]
Declarative programming
Algorithm
s = hcl.create_schedule()
xo, xi = s[out].split(out.x, factor=M)
s[out].reorder(xi, xo, out.y)
Decoupled customization
Customization primitives
More productive / less labor-intensive
for (int xi = 0; xi < M; xi++)
for (int xo = 0; xo < N/M; xo++)
for (int y = 0; y < N; y++)
for (int r = 0; r < 3; r++)
for (int c = 0; c < 3; c++)
out[xi+xo*M, y] +=
image[xi+xo*M+r, y+c] * kernel[r, c]
Reorder loops
Tile loop

## Slide 6: Decoupled Memory Customization
Primitives can be applied with a user-defined sequence
for (int y = 0; y < N; y++)
for (int x = 0; x < N; x++)
for (int r = 0; r < 3; r++)
for (int c = 0; c < 3; c++)
out[x, y] += image[x+r, y+c] * kernel[r, c]
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))

## Slide 7: Decoupled Memory Customization
for (int y = 0; y < N; y++)
for (int x = 0; x < N; x++)
for (int r = 0; r < 3; r++)
for (int c = 0; c < 3; c++)
out[x, y] += image[x+r, y+c] * kernel[r, c]
Primitives can be applied with a user-defined sequence
image
linebuffer
out
y
x
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))
s = hcl.create_schedule()
linebuf = s[image].reuse_at(out, out.y)

## Slide 8: Decoupled Memory Customization
winbuf = s[linebuf].reuse_at(out, out.x)
for (int y = 0; y < N; y++)
for (int x = 0; x < N; x++)
for (int r = 0; r < 3; r++)
for (int c = 0; c < 3; c++)
out[x, y] += image[x+r, y+c] * kernel[r, c]
Primitives can be applied with a user-defined sequence
image
linebuffer
out
y
x
window buffer
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))
s = hcl.create_schedule()
linebuf = s[image].reuse_at(out, out.y)

## Slide 9: Decoupled Memory Customization
Primitives can be applied with a user-defined sequence
image
linebuffer
for (int y = 0; y < N; y++)
for (int x = 0; x < N; x++)
for (int r = 0; r < 3; r++)
for (int c = 0; c < 3; c++)
out[x, y] += image[x+r, y+c] * kernel[r, c]
out
y
x
window buffer
kernel
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))
winbuf = s[linebuf].reuse_at(out, out.x)
s = hcl.create_schedule()
linebuf = s[image].reuse_at(out, out.y)

## Slide 10: Decoupled Data Type Customization
s = hcl.create_scheme()
s.quantize([out], Fixed(6, 4))
Bit-accurate data type support (e.g., Int(15), Fixed(7,4))
Decoupled customization primitives: downsize & quantize
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))

## Slide 11: Decoupled Data Type Customization
Bit-accurate data type support (e.g., Int(15), Fixed(7,4))
Decoupled customization primitives: downsize & quantize
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))
for i in range(2, 8):
s = hcl.create_scheme()
s.quantize([out], Fixed(i, i-2))
Chart: Total bitwidth
| 2 | 3 | 4 | 5 | 6 | 7 | 8
activation | 9.8 | 65.77 | 98.25 | 98.74 | 98.74 | 98.82 | 98.83
Trade-off between accuracy and resource for a neural network

## Slide 12: Currently Supported Customization Primitives
Compute customization
Data type customization
Memory customization
Macros for spatial architecture templates

## Slide 13: Macro for Stencil with Dataflow Architecture
A sliding window applied on a tensor
For applications where data elements are updated with some fixed, local patterns
Incorporate with SODA [Y. Chi, et al. ICCAD’18]
  Scalable reuse buffers with minimum buffer size that achieve highest throughput
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))
s = hcl.create_schedule()
s[out].stencil()
RB
RB
RB
RB
RB
RB
RB
RB
RB
RB
RB
Pipelined reuse buffers (RB)

## Slide 14: Macro for Systolic Array
A group of PEs locally connected to each other
For applications having perfectly nested loops with uniform dependency
Incorporate with PolySA [J. Cong, et al. ICCAD’18]
  Systematic and efficient design space exploration => Comparable performance to manual designs within hours
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Loader
On-chip BRAMs
Off-chip DDRs
[X. Wei, et al. DAC’17]
r = hcl.reduce_axis(0, 3)
c = hcl.reduce_axis(0, 3)
out = hcl.compute(N, N),
lambda y, x:
hcl.sum(image[x+r, y+c]*kernel[r, c],
axis=[r, c]))
s = hcl.create_schedule()
s[out].systolic()

## Slide 15: Imperative Programming in HeteroCL
HeteroCL further provides an embedded imperative DSL
  Not all algorithms can be described using declarative code
Unified interface for applying hardware customization to both imperative and declarative codes
with hcl.for_(0, N) as y:
with hcl.for_(0, N) as x:
with hcl.for_(0, 3) as r:
with hcl.for_(0, 3) as c:
out[x, y] += image[x+r, y+c] * kernel[r, c]
We need DSL because normal Python is too flexible (i.e., not all semantics are synthesizable)
s = hcl.create_schedule()
s[out].split(out.x, M)
linebuf = s[image].reuse_at(out, out.y)
s.quantize([out], Fixed(6, 4))
# …

## Slide 16: Explore the Interdependence: Dot Product
i = hcl.reduce_axis(0, N)
return hcl.compute((1,),
lambda x: hcl.sum(local_A[i] * local_B[i],
axis=i))
DMA
Off-chip memory
dot_product
local_A
local_B
PE
PE
…
+
+
output
NUM_PE
Compute throughput
NUM_PE
#Elem / IO access
W=8
W=16
W=32
,
= min(
)
NUM_PE
Performance
W=32
W=16
W=8
for W in [4, 8, 16, 32]:
NUM_PE = BANDWIDTH / W
xo, xi = s[psum].split(x, NUM_PE)
s[psum].unroll(xi)
s.quantize(local_A, hcl.Fixed(W))
s[local_A].partition(NUM_PE)
Memory
Data type
Compute
NUM_PE
PE
W
+
BANDWIDTH

## Slide 17: HeteroCL Compilation Flow
HeteroCL
B = h.compute((10,),
lambda x: A[k] + 2)
s = h.create_schedule()
s[B].unroll(B.axis[0])
Extended TVM/Halide IR
produce B {
unrolled (x, 0, 10) {
B[x] = (A[x] + 2)
}
}
Merlin C Compiler
General Back End
LLVM Code Generation
CPU
HLS Code Gen
Cloud FPGAs
Embedded FPGAs
PolySA
SODA
Spatial Architectures
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Loader
RB
RB
RB
RB
RB
RB
RB
RB
RB
RB
RB
image
image
image
out
out
out

## Slide 18: Evaluation with Amazon AWS f1
Benchmark | Application Field | + stencil | + unroll | + quantize | Theoretical (limited by memory bandwidth)
Seidel | Image processing | 0.2 | 2.9 | 5.9 | 6.8
Gaussian | Image processing | 1.1 | 6.7 | 13.2 | 15.6
Jacobi | Linear algebra | 0.4 | 2.3 | 5.0 | 5.4
Benchmark | Application Field | Back end | Data type | Performance (GOPs) | Speedup
GEMM | Matrix multiplication | CPU (Intel MKL) | float32 | 76.0 | 1.0
 |  | FPGA | float32 | 245.9 | 3.2
 |  |  | fixed16 | 807.6 | 10.6
LeNet | Convolutional neural network | CPU (TVM TOPI) | float32 | 15.4 | 1.0
 |  | FPGA | float32 | 79.8 | 5.2
 |  |  | fixed16 | 137.8 | 8.9
Stencil
Systolic
Benchmark | Application Field | Speedup
KNN Digit Recognition | Image classification | 12.5
K-Means | Clustering | 16.0
Smith-Waterman | Genomic sequencing | 20.9
General
Rapidly achieve good speedup for a rich set of applications

## Slide 19: Case Study: Binarized Neural Network (BNN)
ECE 5775 (high-level digital design automation) at Cornell [1]
  34 students: graduates and senior undergrads
In-class competition: higher speedup => higher score
  Baseline: unoptimized BNN on ARM (Zynq)
  Time: two weeks
Chart: Speedup
| <10x | 10~20x | 20~30x | 30~40x | 40~50x | >50x
 | 20 | 8 | 4 | 0 | 0 | 2
[1] https://www.csl.cornell.edu/courses/ece5775/

## Slide 20: Optimized BNN in HLS C
template<int M, int N, int I, int L>
void conv(ap_int<32> input[MAX_FMAP_PACK_SIZE],
ap_int<32> output[MAX_FMAP_PACK_SIZE],
const ap_int<8> threshold[MAX_FMAP],
hls::LineBuffer<F, I, bit> buf[M]) {
int O = I - F + 1, ifmap_size = I * I, ofmap_size = O * O;
hls::Window<F, F, bit> window[M];
for (int y = 0; y < O; y++) {
for (int m = 0; m < M; m++) {
#pragma HLS pipeline
for( int x = 0; x < F - 1; x++) {
int i_index = x + (y + F - 1) * I + m * ifmap_size;
bit newBit = GET_BIT(input, i_index, PACK_WIDTH_LOG);
fillBuffer<F, I>(window[m], buf[m], x, newBit);
}}
for (int x = 0; x < O; x++) {
for (int m = 0; m < M; m++) {
int i_index = x + F - 1 + (y + F - 1) * I + m * ifmap_size;
bit newBit = GET_BIT(input, i_index, PACK_WIDTH_LOG);
fillBuffer<F, I>(window[m], buf[m], x + F - 1, newBit);
}
for (int n = 0; n < N; n++) {
#pragma HLS pipeline
int sum = 0;
int o_index = x + y * O + n * ofmap_size;
for (int m = 0; m < M; m++) {
int one_out = 0, mac_num = 0;
for (int c = 0; c < F; c++) {
for (int r = 0; r < F; r++) {
if (if_mac(x + c, y + r, I)) { //neglect padding pixels in mac
int i_index = x + c + (y + r) * I + m * ifmap_size;
int w_index = c + r * F + (n + m * N) * FILTER_SIZE;
if (L == 0) one_out += window[m].getval(r, c) == w_conv1[w_index];
else one_out += window[m].getval(r, c) == w_conv2[w_index];
mac_num++;
}}}
sum += (one_out << 1) - mac_num;
}
SET_BIT(output, o_index, PACK_WIDTH_LOG, sum > threshold[o_index] ? 1 : 0);
}}}}
Compute customization
Data type customization
Memory customization
Applied customization techniques
Compute: tiling, pipelining, reordering
Data type: bit packing
Memory: partitioning, line buffer, window buffer

## Slide 21: Optimized BNN in HeteroCL
Development time: < 3 days
Final speedup: 63x
rc = hcl.reduce_axis(0, in_fmaps)
ry = hcl.reduce_axis(0, F)
rx = hcl.reduce_axis(0, F)
C = hcl.compute((1, out_fmaps, O, O),
lambda nn, ff, yy, xx:
hcl.select(
hcl.sum(A[nn,rc,yy+ry,xx+rx] * B[ff,rc,ry,rx], axis=[rc,ry,rx]) >
threshold[nn,ff,yy,xx], 1, 0 ),
dtype=hcl.UInt(1))
s.quantize(C, hcl.UInt(32))
s[C].split(C.axis[1], factor=5)
s[C].unroll(C.axis[2], factor=5)
s[C].pipeline(C.axis[3])
lb = s[A].reuse_at(C, C.axis[0])
wb = s[lb].reuse_at(C, C.axis[1])
✓ More productive
✓ More maintainable

## Slide 22: Conclusions
HeteroCL is a multi-paradigm programming infrastructure
  Decouples algorithm from compute, data type, and memory customization
  Provides an abstraction capturing the interdependence and trade-offs
Maps to spatial architecture templates with macros
  Stencil with dataflow architecture
  Systolic array
Validated against a rich set of benchmarks from multiple domains
  Image processing, linear algebra, deep learning, etc.
Algorithm
Compute Customization
Data Type Customization
Memory Customization
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Feeder
Loader

## Slide 23: Next Stop
Connecting with front-end DSLs
  E.g., PyTorch & MXNet
Open source release of HeteroCL is coming soon!

## Slide 24
HeteroCL
Yi-Hsiang Lai1, Yuze Chi2, Yuwei Hu1, Jie Wang2, Cody Hao Yu2,3, Yuan Zhou1, Jason Cong2, Zhiru Zhang1
1Cornell University, 2University of California, Los Angeles, 3Falcon Computing Solutions, Inc.
Questions?