## Slide 1: F5-HD: Fast Flexible FPGA-based Framework for Hyperdimensional Computing
Sahand Salamat, Mohsen Imani, Behnam Khaleghi,
Tajana Šimunić Rosing
System Energy Efficiency Lab
University of California San Diego

## Slide 2
Machine Learning is Changing Our Life
Self Driving Cars
Smart Robots
Gaming
Healthcare
Finance

## Slide 3
Hyperdimensional (HD) Computing
Encode
High Dimensional Data
Image Classification
Activity Recognition
Regression
Clustering
...
HyperDimensional
Computing
General and scalable
Robust to noise
Light weight
[1] Kanerva, Pentti. "Hyperdimensional computing: An introduction to computing in distributed representation with high-dimensional random vectors." Cognitive Computation 1.2 (2009): 139-159.
[2] Imani, Mohsen, et al. "Exploring hyperdimensional associative memory." 2017 IEEE International Symposium on High Performance Computer Architecture (HPCA). IEEE, 2017.

## Slide 4: HD Computing
-1 +1 -1 -1 +1 . . . +1
-1 -1 +1 -1 -1 . . . +1
Dog hypervector
Cat hypervector
Encoding
+1 +1 +1 -1 -1 . . . +1
Encoded hypervector
Training
Inference
Similarity Check
. . .
. . .
+
+
+
+
+
+
+
+
Encoding
Encoding
-1 +1 -1 -1 +1 . . . +1
-1 -1 +1 -1 -1 . . . +1
Dog hypervector
Cat hypervector
Retraining
×
-
+

## Slide 5: HD dataflow
    Similarity Check
      Hamming Distance for binary model
      Cosine similarity for non-binary model

## Slide 6: HD Acceleration
HD  thousands of bit-level additions, multiplication and accumulation
  These operations can be parallelized in dimension level
FPGAs can provide huge parallelism
FPGA design requires extensive hardware expertise
FPGAs have long design cycles
  Application-specific template-based design
  Several template-based FPGA implementation for neural networks [Micro’16][FCCM’17][FPGA’18]
  No FPGA implementation framework for HD!
[1] Sharma, Hardik, et al. "From high-level deep neural models to FPGAs." The 49th Annual IEEE/ACM International Symposium on Microarchitecture. IEEE Press, 2016
[2] Guan, Yijin, et al. "FP-DNN: An automated framework for mapping deep neural networks onto FPGAs with RTL-HLS hybrid templates." 2017 IEEE 25th Annual International Symposium on Field-Programmable Custom Computing Machines (FCCM). IEEE, 2017.
[3] Shen, Junzhong, et al. "Towards a uniform template-based architecture for accelerating 2d and 3d cnns on fpga." Proceedings of the 2018 ACM/SIGDA International Symposium on Field-Programmable Gate Arrays. ACM, 2018.

## Slide 7: -HD
F5-HD: Fast Flexible FPGA-based Framework for Refreshing Hyperdimensional Computing
First automated framework for FPGA-based acceleration of HD computing
  Input : <20 lines of C++ code
  Output: >2000 lines of Verilog HDL code
Supports training, retraining, and inference of HD
Kintex, Virtex, Spartan FPGA families
Supports different Precisions
  Fixed-point
  Power of two
  Binary
F5

## Slide 8: F5-HD Overview
Model Specification
Design Analyzer
Model Generator
Scheduler
F5-HD

## Slide 9: Baseline Encoding
S=3
F= 4
HV0 :
HV1 :
HV0
P (HV1)
b
999
b
0
b
1
b
2
b
998
b
997
b
999
b
0
b
1
b
2
b
998
b
997
b
999
b
0
b
1
b
2
b
998
b
997
b
999
b
0
b
1
b
2
b
998
b
997
b
999
b
998
b
0
b
1
b
2
b
997
b
0
b
1
b
2
b
999
b
998
b
997
P 2 (HV0)
P 3 (HV0)
b0HV0+b999HV1+b998HV0+b997HV0
{b2,b1,b0} Encoded HV =
b1HV0+b0HV1+b999HV0+b998HV0
b2HV0+b1HV1+b0HV0+b999HV0
b997,b998,b999,b0,b1,b2 of base HVs are needed
Base Hypervectors

## Slide 10
F5-HD Encoding
S=3
F= 4
HV0 :
HV1 :
HV0
P (HV1)
b
999
b
0
b
1
b
2
b
998
b3
b
999
b
0
b
1
b
2
b
998
b3
P 2 (HV0)
P 3 (HV0)
b0HV0+b1HV1+b2HV0+b3HV0
{b2,b1,b0} Encoded HV =
b1HV0+b0HV1+b2HV0+b3HV0
b2HV3+b1HV2+b0HV1+b0HV0
b0,b1,b2,b3 of base HVs are needed
b
999
b
998
b
0
b
1
b
2
b3
b
0
b
1
b
2
b
999
b
998
b3
b
999
b
998
b
0
b
1
b
2
b3
b
0
b
999
b
998
b
1
b
2
b3
memory bandwidth

## Slide 11: F5-HD Encoder Architecture
+
+
+
+
+
+
b
999
b
0
b
1
b
2
b
998
b
997
b
999
b
0
b
1
b
2
b
998
b
997
b
999
b
0
b
1
b
2
b
998
b
997
+
+
+
+
+
+
b1
b0
Instead of using adders F5-HD uses LUTs
+
+
+
+
+
+
36 bits
#Features
Design Analyzer
Hand
-
optimized
Templates
PU
PE
Encoding
HD Model
Model Generator
Scheduler

## Slide 12: F5-HD Architecture
Hand
-
optimized
Templates
PU
PE
Encoding
HD Model
Design Analyzer
Model Generator
Scheduler

## Slide 13: F5-HD Processing Unit/Engine
Hand
-
optimized
Templates
PU
PE
Encoding
HD Model
Processing Unit
  Finding similarity between input and a class
Processing Engine
  Multiplication and Accumulation
Design Analyzer
Model Generator
Scheduler

## Slide 14
Hand
-
optimized
Templates
PU
PE
Encoding
HD Model
F5-HD Steps: Design Analyzer
Design Analyzer
  Selects the model precision
  Create a power model as a function of parallelization
  maximize the resource utilization with respect to the user’s power budget
  Calculating the parallelization factor
Design Analyzer
Model Generator
Scheduler

## Slide 15: F5-HD steps
Hand
-
optimized
Templates
PU
PE
Encoding
HD Model
Design Analyzer
Model Generator
Scheduler
Model Generator
  Instantiates hand-optimized template modules
  Generates memory interface and Verilog HDL code
Scheduler
  Adds scheduling and controlling signals
F5-HD
module HD (clk, rst, out);
…
MemInterface (…);
InputBuffer (…);
HDEncoder (…);
Training_Retraining (…);
HDModel (…);
AssociativeSearch (…);
Scheduler (…);
Controller (…);
endmodule
module PU(…);
…
endmodule
…
HD.v
Void main () {
//Application
NumInFeatures=700;
NumClasses=5;
NumTrainingData=50000;
…
//User Spec.
PowerBudget=5;
HDModel=“binary”;
//FPGA Spec
FPGA=“XC7k325T ”;
FPGAPowerModel=“p.model”;
…
}
HD.cpp

## Slide 16: Experimental Setup
F5-HD
  Including user interface and code generation has been implemented in C++ on CPU
  Hand-optimized templates implemented in Verilog HDL
  Generates synthesizable Verilog implementation
  Supports Kintex, Virtex, and Spartan FPGA families
Results are compared to
  Intel i7 7600 CPU and AMD R9 390 GPU
Datasets:
  Speech Recognition (ISOLET) [31]
  Activity Recognition (UCIHAR) [32]
  Physical Activity Monitoring (PAMAP) [33]
  Face Detection [34]

## Slide 17: Experimental Results
F5-HD reduces the design time significantly
  Writing FPGA implementation takes >100 days (>2000 lines of code) [FPL’16]
  Preparing F5-HD input takes < 1 hour (<20 lines of code)
F5-HD is 5.1x faster than HLS implemented hardware
Kapre, Nachiket, and Samuel Bayliss. "Survey of domain-specific languages for FPGA computing." 2016 26th International Conference on Field Programmable Logic and Applications (FPL). IEEE, 2016.
Chart: Throughput
| Face | UCIHAR | PAMAP | ISOLET
HLS | 483.1 | 478.5 | 473.9 | 465.1
F5-HD | 4687.5 | 2734.4 | 1562.5 | 781.3
*10 3

## Slide 18: Experimental Results: Encoding
F5-HD encoder
  For 64 features: 1.5× higher throughput
  For 512 features: 1.9× higher throughput
Chart: Maximum encoding capacity (dimensions/cycle)
| 64 | 128 | 256 | 512
Baseline | 975 | 449 | 254 | 110
F5-HD Encoder | 1505 | 837 | 481 | 211

## Slide 19: Experimental Results: Training
F5-HD vs GPU:
  87× more energy efficient
  8× faster
F5-HD vs CPU:
  548x more energy efficient
  148x faster

## Slide 20: Experimental Results: Retraining
F5-HD vs GPU:
  7.6× more energy efficient
  1.6× faster
F5-HD vs CPU:
  70x more energy efficient
  10x faster

## Slide 21: Experimental Results: Inference
Energy and execution time improvement during inference
  2X, 260X faster than GPU, and CPU
  12X, 620X more energy efficient than GPU and CPU

## Slide 22: Experimental Results: HD precision
Binary HD is 4.3x faster but 20.4% less accurate than fixed-point model
Power of two model is 3.1x faster but 5.8% less accurate than fixed point model
Accuracy | ISOLET | UCIHAR | PAMAP | FACE
Binary HD | 88.1% | 77.4% | 85.7% | 48.5%
Power-of-two HD | 90.3% | 88.0% | 90.8% | 89.6%
Fixed-point HD | 95.5% | 94.6% | 94.5% | 96.9%

## Slide 23: Conclusion
F5-HD: an automated framework for FPGA-based acceleration of HD computing
F5-HD reduces the design time from 3 months to less than an hour
F5-HD supports:
  Fixed-point, power of two and binary models
  Training, retraining, and inference of HD
  Xilinx FPGAs
F5-HD is:
  ~5x faster than HLS tool implementation
  ~87x more energy efficient and ~8x faster during training than GPU
  12x more energy efficient and 2x faster during inference than GPU