## Slide 1: System View Inc.

## Slide 2: Problem
Embedded Systems
Getting Increasingly Complex
System Design Span Multiple Chips (CPUs, GPUs, FPGAs, DSPs ….)
Difficult to Integrate, No Visibility
No Universal Tool Exists for Integration
Notes: Continued push towards higher integration
2) FPGAs see the variety of Systems . FPGAs are not alone in system. ,. FPGAs are used for I/O s . Horizontal tool support
3) Interfaces difficult to bring-up & debug. 2 Cavium + 56 FPGA
4) Multi-level failure software (thread-locking) , hardware (fifo overflow), data corruption .. Don’t know what is going on
4) What-if requires massive changes
5) Project failed due to long integration time.

## Slide 3: Solution: Visual System Integrator
Rapid, visual application development:
Describe Hardware platform.
Develop Application (Import C/C++/RTL blocks connect them)
Automatic code generation for the complete system (Software/Hardware projects, drivers, DMAs)
Get unprecedented Transaction level visibility at runtime
Focus on your application, not the platform & firmware!
Notes: Why Visual ? Natural people draw diagrams to describe their systems . NI (Labview) & Mathworks (Simulink)
Increases ease of use & raise the abstraction without loosing I/O advantage / differentiation . Raising to much can cause questions
Enable both FPGA skilled & Software skilled
System level visibility important, chip level debug available hard to correlate events from across the system (light weight monitoring), no jtag
5) Components come-in out of order. Two benefits our tool used in portions only , increases adoption

## Slide 4: Design Visualization : Platform & System Layers
Platform Layer
  Board level Physical Hardware
  Express connections & transport between Physical entities
Application / System Layer
  Easily add logical blocks
  Import C/C++/Java or Python code
  Connect blocks to express dataflow
Notes: Why Visual ? Natural people draw diagrams to describe their systems . NI (Labview) & Mathworks (Simulink)
Increases ease of use & raise the abstraction without loosing I/O advantage / differentiation . Raising to much can cause questions
Enable both FPGA skilled & Software skilled
System level visibility important, chip level debug available hard to correlate events from across the system (light weight monitoring), no jtag
5) Components come-in out of order. Two benefits our tool used in portions only , increases adoption

## Slide 5: Visual System Integrator: Work Flow
Describe
Hardware
Platform
(Import Existing)
Compile
Platform
Platform
Meta data
Software Projects
Eclipse, Qt, VC++ , …
Import
Platform
FPGA
Projects
Develop
Application
System
Compile Generate System
Runtime , Drivers &
OS Configurations …

## Slide 6: VSI Built Systems

## Slide 7: Load On Demand (Partial Reconfig)
Time multiplex hardware Resource [R5, FPGA Fabric … ]
Dynamically change the behavior of a system
  Radar : Transmit, Receive or Communication
  Deep Learning: Reconfigure between Training vs Evaluation
  Self Driving Car: Adapt to different driving /weather conditions
              Snow, Rain, Highway, City etc

## Slide 8: Load On Demand
  Load on Demand using Data-Flow
G1
G1
Forward
Camera Display
Rear
Camera
Display
Forward Camera
Processing
Rear Camera
Processing
Gear
Spindle

## Slide 9: Load On Demand
  Load on Demand using Data-Flow
G1
G1
Forward
Camera
Display
Rear
Camera
Display
Forward Camera
Processing
Rear Camera
Processing
Gear
Spindle
A
B
Fixed
vsi::runtime

## Slide 10: Load On Demand
Action | Time in uS (10e-6 Seconds)
Config Block Setup | 210 uS
Decouple Logic from Active | 123 uS
Load Partial Bitstream (~1.2Mbytes) | 19845 uS
Recouple Logic to Active | 138 uS
Restore Config block setup | 77 us
Total | 20393 uS (.02 S)

## Slide 11
User C/C++ Code
DSP
Function
X86
FPGA
Import Platform
Software
Library
FPGA
Library
C/C++
Functions
Develop Application
Synthesizable
C/C++ Function
TCP
SERVER
Synthesizable
C/C++ Function
Application Development : Example

## Slide 12
System Level Verification: Transport
CPU
Embedded
CPU
CPU (X86)
Simulator
FPGA
FPGA
Emulator
Shared
Memory
TCP/IP
PCI/e
AXI (Zynq)
Aurora
Pin Muxing
Transaction Based
(DPI over TCP/IP)
Transaction Based
(Transactor)
PCI/e

## Slide 13
System Level Verification
CPU
Embedded
CPU
CPU (X86)
Simulator
FPGA
FPGA
Emulator
C/C++
C/C++
Java
Python
C/C++
Java
Python
Synthesizable
C/C++
Synthesizable
C/C++
Synthesizable
C/C++
Synthesizable
C/C++
Synthesizable
C/C++
Synthesizable
C/C++
RTL
RTL
RTL
RTL

## Slide 14: Rapid Application Development using Visual System Integrator
Real Time tracking of Optical & Thermal images
Capture V4L
Capture ROI
xf::MeanShift
Track ROI
Display
Webcam Image
Xilinx: UltraScale MPSoC: Iveia Captiva
CPU (ARM64)
FPGA
USB
Quad SPI
Display
FFT
FFT
Capture Microphone
Samples
SPI
Thermal
Image Capture
xf::MinMax
Display
Thermal Image
SPI