## Slide 1: Network-on-Chip Programmable Platform in Versal™ ACAP Architecture
Ian Swarbrick, Dinesh Gaitonde, Sagheer Ahmad, Brian Gaide, Ygal Arbel
Xilinx Silicon Architecture Team

## Slide 2: Agenda
Versal Devices and Motivation for Hardened NoC
Overview of Versal NoC
Timing Closure Benefits
Routing
Conclusions

## Slide 3: Versal Device
Versal – Xilinx 7nm Generation Devices
Adaptive Compute Acceleration Platform (ACAP) devices
Device-wide hardened NoC
Each physical link has full-duplex paths
  128 bit data @ 1 GHz at mid-speed grades.
All resource address mapped
  Configurable address map
Note: not an actual device

## Slide 4: Motivation for Hardened NoC
Need for efficient data movement
  Data movement common across all applications.
  Wires not scaling with logic.
  Data movement needs to keep up with memory.
    ~100 GB/sec DDR
    Hundreds of GBs/sec with HBM
  Increasing wire delays make timing closure harder.
Move towards Platform with fabric
  All fabric ports and hard IP are globally addressable from anywhere on the device.
  Independent from fabric and available without loading any fabric bitstream.

## Slide 5: Overview of Versal NoC

## Slide 6: Hardened NoC – Packetized Interconnect
Packetize, transport, de-packetize
Virtual Channels provide independent non-blocking flow control

## Slide 7: NoC Topology
HNoC – 4 or 2 Physical Lanes
  64 GBytes/sec at in each direction 1GHz
VNoC – 2 Physical Lanes
  32 GBytes/sec in each direction at 1GHz
Each NoC lane (physical channel) is 2 full-duplex links.
  16 GBytes/sec raw bandwidth (@ 1GHz)
HNoCs connect up/down to hard IPs
VNoCs connect horizontally to fabric
Note: not an actual device

## Slide 8: NoC Scaling
Bigger devices need more NoC resources
Wider devices have more IO on the top and bottom of the device
One VNoC column per DDR channel
  More fabric -> NoC connects is device width grows.
  More vertical bandwidth as device width grows.
Taller devices have more fabric
  Each half-FSR (fabric sub-region) in VNoC has one ingress and one egress NoC path.
  More fabric/NoC connections as device height grows.
MC
MC
MC
MC
MC
Horizontal Scaling
Vertical Scaling

## Slide 9: NoC for Multi-Die Devices
NoC extends across SSIT (Stacked Silicon Interconnect Technology) devices
VNoC physical channels continue across devices
Source synchronous, single data rate links across interposer

## Slide 10: NoC Quality-of-Service
Routes through network are programmable
Each route is assigned to a traffic class
Classes separated using virtual channels
Traffic classes can be:
  Low latency (reads): prioritize traffic to give low latency without compromising other QoS constraints.
  ISOC: Bounded latency.
  Best Effort: given whatever service is available.
Other mechanisms provide traffic shaping
  Ingress rate control
  Weighted arbitration at every NoC switch.

## Slide 11: QoS Example
(GB/sec)
Notes: Ask, compiler flow, simulation.

## Slide 12: NoC Timing Closure Benefits

## Slide 13: Timing Closure
Fabric timing closure requires iteration
Hardened NoC interfaces and modular design simplify the process
Chart: Normalized BW per Channel
| A | B | C | D
Soft 2x2 | 0.65129 | 0.57788 | 0.52141 | 0.61365
NOC 2x2 | 1 | 1 | 1 | 1

## Slide 14: NoC Routing

## Slide 15: NoC Routing
Versal NoC has distributed routing tables
QoS managed per-connection
Dynamically re-programmable for partial reconfiguration
Tools take user QoS constraints and configure paths
Routes created in a deadlock-free manner

## Slide 16: NoC Compiler
Compiler takes in user traffic and design constraints (including NoC topology)
Produces routing assignments that
  Meet QoS specification
  Are deadlock free

## Slide 17: Hardened NoC Example
4 DDR Memories interleaved
16 Fabric masters
External bandwidth from PCIe
  Local processor control traffic also
~150 GBytes/sec aggregate bandwidth
NoC compiler runs in minutes
No fabric resources consumed for routing/address/switching or DDR

## Slide 18: Conclusions

## Slide 19: Versal NoC - Conclusions
Hardened NoC that scales across Versal product family
Eases timing closure and increases design productivity
Flexible QoS
Programmable route and bandwidth assignments
A core infrastructure piece of the Versal ACAP platform